## Slide 1: Transradial Prosthetic Arm
Henry Lather
Team Members: Kendall Gretsch and Kranti Peddada
Mentors: Dr. Charles Goldfarb and Dr. Lindley Wall
Website: www.transradialprostheticarm.weebly.com

## Slide 2: Transradial Limb Amputation
preview.turbosquid.com
1/3 proximal

## Slide 3: Need
There are an roughly 10,000 individuals in the US with a transradial limb difference
Most are highly functional, even without a prosthesis
However, many want a prosthesis to augment function
The goal is to give the user a sense of normality and to allow the user to multitask

## Slide 4: Design Specifications
Patient Population
  Unilateral, transradial limb difference
  Ages 5+
Total Parts Cost
  Maximum $150
Joints
  Fingers at least one
  Thumb has two
  1 degree of freedom per joint
Comfort
  Does not cause pain, skin abrasions, or infection

## Slide 5: Design Specifications (cont.)
Functionality
  Fingers and thumb open and close at least at the mouth, belt, and out front
  Independent thumb movement with key grip
  Ability to lift and hold at least 500 g
Donning and Doffing
  Independently in under 30 seconds
Security
  Does not come off unless intentionally removed
Weight
  Does not exceed weight of missing limb

## Slide 6: Design Components We Evaluated
Final Design
Actuation and Control
Socket Design and Fabrication
Suspension
Terminal Device

## Slide 7: Design Components We Evaluated
Final Design
Actuation and Control
Socket Design and Fabrication
Suspension
Terminal Device

## Slide 8: Actuation and Control Design Options
Body-powered
  Shoulder-controlled
  Elbow-controlled
Externally-powered
  Shoulder-controlled
  Voice-controlled
  Button-controlled
  EMG-controlled

## Slide 9: Body-powered, Shoulder- controlled
3 separate movements
Uncomfortable
Hard to use

## Slide 10: Body-powered, Elbow-controlled
2 separate movements
Very limited range of motion

## Slide 11: Externally-powered, Shoulder-controlled
Sensor
Sensor can distinguish 2 independent movements

## Slide 12: Externally-powered, Voice-controlled
Microphone
Socially disruptive
Would not work in high-noise places

## Slide 13: Externally-powered, Button-controlled
Buttons
Simple and reliable
Requires use of other hand

## Slide 14: Comparison of General Features
Body-powered
Uncomfortable
Can fatigue user
Hard to use
Mechanical parts visible
Hard to Don/Doff
Low cost
Light-weight
Durable
Externally-powered
Comfortable
No fatigue
Easy to use
Mechanical parts hidden
Easy to Don/Doff
Higher cost
Heavier
Less durable









## Slide 15: Comparison of General Features (cont.)
Body-powered
Low maintenance
Easily scales to different sizes
Sensory feedback through effort
Externally-powered
Higher maintenance
Electronic components do not easily scale
No sensory feedback




## Slide 16: Pugh Chart Selection
Actuation and Control |  | Body-powered |  | Externally-powered |  | 
 | Weight | Shoulder | Elbow | Shoulder | Voice | Button
Hinderance to Daily Life | 10 | 7 | 3 | 10 | 2 | 2
Comfort | 9 | 1 | 4 | 9 | 10 | 10
Cost | 8 | 10 | 10 | 5 | 5 | 6
Ease of Use | 7 | 4 | 1 | 10 | 10 | 10
Aesthetics | 7 | 2 | 5 | 10 | 10 | 9
Weight | 6 | 10 | 10 | 5 | 5 | 7
Force | 6 | 8 | 7 | 6 | 6 | 6
Don/Doff Time | 6 | 1 | 3 | 8 | 10 | 10
Durability | 4 | 9 | 10 | 7 | 7 | 7
Maintenance | 4 | 8 | 9 | 6 | 5 | 7
Scalability | 2 | 7 | 7 | 5 | 5 | 5
Sensory Feedback | 1 | 9 | 9 | 2 | 2 | 2
Total |  | 406 | 407 | 539 | 476 | 497
Our mentors strongly preferred the Externally-powered, Shoulder-controlled device as well

## Slide 17: Design Components We Evaluated
Final Design
Actuation and Control
Socket Design and Fabrication
Suspension
Terminal Device

## Slide 18: Socket Design and Fabrication: 3D Printed Socket Chosen
Custom made
  Maximize fit and comfort
Process
  3D scan of residual limb
  Negative of scan for socket model
  Print
Fast and inexpensive
Less durable than traditional socket
http://store.solidoodle.com/

## Slide 19: Design Components We Evaluated
Final Design
Actuation and Control
Socket Design and Fabrication
Suspension
Terminal Device

## Slide 20: Suspension System Chosen
Sock liner with locking pin
Sock slides on easily with one hand
Locking pin secures socket to limb
http://www.easyliner.com

## Slide 21: Design Components We Evaluated
Final Design
Actuation and Control
Socket Design and Fabrication
Suspension
Terminal Device

## Slide 22: Terminal Device Options
Customizable Terminal Devices
  Robohand
  Single joint, Lever-based Hand
  The Mitten
Commercial Terminal Devices
  TRS Hook (Buy)
  Hosmer APRL Hook (Buy)
  Hosmer APRL Hand (Buy)
  Soft Hands (Buy)

## Slide 23: The Robohand
Existing low-cost solution
Open-source CAD files
2 joints in each finger
http://www.thingiverse.com/thing:92937

## Slide 24: Single Joint, Lever-based Hand
Designed by our team
Similar in form and function to the Robohand

## Slide 25: Single Joint, Lever-based Hand
Each finger has two levers
  One for restoring force
  One for actuating force
Apply Tension

## Slide 26: The Mitten
Modeled closely after the Robohand
All 4 fingers move as one unit

## Slide 27: Hooks
Efficient
Unsightly

## Slide 28: Hosmer APRL Hand
Decent in all categories
Expensive to buy

## Slide 29: Functional "Soft" Hands
Soft, skin-like covering over metal hook
Extremely life-like appearance
Extremely expensive

## Slide 30: Pugh Chart Selection
Terminal Devices |  | Customizable Hands |  |  | Commercial Devices |  |  | 
 | Weight | RoboHand | Lever-based | Mitten | TRS Hook | APRL Hook | APRL Hand | Soft Hand
Cost | 10 | 10 | 10 | 10 | 6 | 4 | 4 | 1
Aesthetics | 10 | 6 | 4 | 3 | 1 | 1 | 9 | 10
Weight | 8 | 10 | 10 | 10 | 7 | 8 | 6 | 5
Efficiency | 6 | 5 | 6 | 6 | 10 | 7 | 7 | 1
Durability | 4 | 2 | 3 | 4 | 10 | 9 | 7 | 6
Repair Cost | 3 | 10 | 10 | 10 | 1 | 1 | 1 | 1
Total |  | 308 | 298 | 292 | 229 | 195 | 251 | 183
Our mentors were not enthusiastic about The Mitten
We decided to go with the Robohand because it scored the highest and it has already been proven to work

## Slide 31: Chosen Design Components
Final Design
Externally-powered, shoulder-controlled
3D Printed Socket
Sock Liner with Locking Pin
The Robohand

## Slide 32: Chosen Design Components
Final Design
Externally-powered, shoulder-controlled
3D Printed Socket
Sock Liner with Locking Pin
The Robohand

## Slide 33: Externally-powered, Shoulder-controlled
IMU
IMU measures linear acceleration and angular velocity

## Slide 34: Our Chosen Design
General electronics schematic
Inertial measurement unit = IMU
Shoulder Movement
IMU
Thumb Stepper Motor
Fingers Stepper Motor
Shoulder Movement
Data
Micro-controller and Motor Controller
Power Supply

## Slide 35: Specific Details of Chosen Design: Possible Components
Arduino R3 Motor Controllers
The Arduino Micro
Adafruit Stepper Motors
Arduino Compatible IMU

## Slide 36: Cable-spooling Method
Rotational actuator
Cable is attached to drive shaft
Winds around drive shaft to increase tension when motor is activated
Motor ON
Tension Applied
Spooling

## Slide 37: Design Schedule

## Slide 38: Team Responsibilities
Kendall Gretsch
  Preliminary Oral Report
  Correspondence with clients
  CAD files
  Socket and Suspension Design
  3D Printing
Henry Lather
  Progress Oral Report
  Webpage Design and Maintenance
  Correspondence with Dr. Klaesner and Leah Vandiver
  Software Development
  Electronics and Robotics Design
Kranti Peddada
  Final Oral Report
  Weekly Updates
  Safety Analysis
  Electronics and Robotics Design

## Slide 39: Sources
http://www.hanger.com/prosthetics/services/upperextremity/Pages/FCI.aspx
http://www.amputee-coalition.org/inmotion/jul_aug_01/primer.html
http://www.hanger.com/prosthetics/services/Technology/Pages/Insignia.aspx
http://madebybump.org/#intro
http://www.amputee-coalition.org/inmotion/nov_dec_04/sockettech.html
http://www.openprosthetics.org/suspension
http://www.ossur.com/?PageID=13412
http://www.nlm.nih.gov/cgi/mesh/2011/MB_cgi?mode=&term=Supination
www.vistatek.com
http://www.solidconcepts.com/resources/dg/injection-molding-design-guidelines/
http://www2.mae.ufl.edu/designlab/Lab%20Assignments/EML2322L-Tolerances.pdf
http://www.solidconcepts.com/resources/dg/injection-molding-design-guidelines/
http://sheldonbrown.com/cables.html

## Slide 40: Questions?